## Slide 1: Channels
DSM2 Training
September 15-17, 2009
Eli Ateljevich, PhD
Delta Modeling Section
California Department of Water Resources

## Slide 2: Topics
Channel networks and geometry
Computational grid
Geometry nuances
Model setup and parameters
New in version 8
Gotchas
Tutorial 1 Intro

## Slide 3: Channel Network

## Slide 4: Channel Network
Channels and nodes
Direction “mostly” seaward/downstream
67
Node
68
Channel
78
Up
Down

## Slide 5: CHANNEL Table
Network connectivity
Friction and Dispersion
CHANNEL
CHAN_NO LENGTH MANNING DISPERSION UPNODE DOWNNODE
1 15000 0.035 0.3 1 2
2 15000 0.035 0.3 2 3
3 15000 0.035 0.3 3 4
2004 15000 0.035 0.3 4 5
5 18000 0.035 0.3 5 6
6 12000 0.035 0.3 6 7
END

## Slide 6: Channel Geometry

## Slide 7: Channel Geometry

## Slide 8: How DSM2 Depicts Geometry
XSECT_LAYER
CHAN_NO DIST ELEV AREA WIDTH WET_PERIM
123 0.5 -14.6 0.0 0.0 0.0
123 0.5 -9.2 216.0 80.0 102.5
123 0.5 -4.0 736.0 120.0 111.0
123 0.5 9.5 2410.0 160.0 142.3
123 0.5 12.0 3028.5 162.0 148.0
END

## Slide 9: Discretization in HYDRO
User requests a spatial step X
Nodes/reach length affect X :
  Actual X smallest subdivision ≥ requested
Computational points
Geometry interpolated to comp points and centers

## Slide 10: User vs Computational

## Slide 11: Interpolation Rules?
Every channel must have one x-sect.
Interpolation is done between x-sects.
If dead end or multi-channel node, the last available X-sect is extended.
Interpolation is linear and based on height from bottom

## Slide 12: Height-based Interpolation
Desired bottom elevation
Interpolated elevation
Adjusted Xsect
Similar volume

## Slide 13: Geometry Gotchas
Providing more x-sects than the model can use.
Including unusual x-sects instead of representational
Uneven bottom elevations due to “pits”

## Slide 14: Other Channel Data
Friction (Mannings n)
Dispersion (out of scope for this class)
  IS flow dependent
  Is NOT classic Dispersion
  See Annual Report Chapter

## Slide 15
http://baydeltaoffice.water.ca.gov/modeling/deltamodeling/annualreports.cfm
QUAL dispersion coefficients 2008 CH2
82-year planning tide 2007 CH4
SDIP gates 2006 CH6
PTM for fish entrainment 2006 CH10
Fingerprinting 2005 CH6, 2002 CH14
Net Delta Outflow calcs using DSM2 & CalSim 2003 CH4
Adjusted astronomical tide 2001 CH10
Annual Reports to SWRCB
DSM2 Cool Tip
SWRCB = State Water Resources Control Board SDIP=South Delta Improvements Program PTM = Particle Tracking Model

## Slide 16: Model Setup for Channels
Specify connectivity in CHANNEL table
  Also Manning and dispersion
In same file, two possible formats for X-sects
  Xsect-Layer (single file format)
  Cross Section Development Program
    (references to csdp files)
Default initial condition (CHANNEL_IC table) required

## Slide 17: For Version 6 Users
QUAL reads geometry from tidefile
Geometry precision issues fixed
  Model runs MUCH faster
No “regular” and “irregular” formats
  They were inconsistent
Don’t convert standard Delta grid
  Adapt your boundary conditions
  We will cover how to convert your other geometry

## Slide 18: Loose Ends: Boundaries
Hydro requires a flow or stage boundary condition at every external node
  Silent default is Q=0: no flow
Qual: concentration for every inflow
Internal node compatibility conditions: continuity and water surfaces match
We will return to this topic!!

## Slide 19: Tutorial 1: Channels
Basic model setup for HYDRO and QUAL
Introduction to channel and cross section formats
Easy intro to the model TABLE syntax and structure
Boundary conditions are steady